## Slide 1
Lecture 9: Memory Mapped Inputs and Outputs
and Simple Peripherals
.

## Slide 2: Overview of Lecture
What Are Peripherals?
Memory Mapped I/O
General Purpose Inputs/Outputs
  Light Emitting Diodes (LEDs)
  Switches
  Keypads
  Liquid Crystal Displays (LCDs)

## Slide 3: ARM Microcontroller Block Diagram
CPU

## Slide 4: ARM Microcontroller Block Diagram
Memory
CPU

## Slide 5: ARM Microcontroller Block Diagram
Memory
Peripherals
CPU

## Slide 6: What Is a Peripheral? Something That Helps the CPU

## Slide 7: What Is a Peripheral?
1. They do something that the CPU does not want to do
Assist a microcontroller CPU by doing some activity in parallel to the CPU's execution of instructions

## Slide 8: What Is a Peripheral?
1. They do something that the CPU does not want to do
Assist a microcontroller CPU by doing some activity in parallel to the CPU's execution of instructions
2. Do things that a microcontroller CPU cannot do
The CPU is a self-contained, digital logic block. There are some things that the CPU just cannot do without help.

## Slide 9: Embedded Systems Challenges
Small Size, Low Weight
      Hand­held electronics
      Transportation applications weight costs money
Low Power
Battery power for 8+ hours (laptops often last only 2 hours)
Limited cooling may limit power even if AC power available
Harsh environment
Heat, vibration, shock
Power fluctuations, RF interference, lightning
Water, corrosion, physical abuse
Safety-critical operation
Must function correctly
Must not function incorrectly
Extreme cost sensitivity
$0.05 adds up over 1,000,000 units

## Slide 10: Interfacing Peripheral Devices to the Processor
Connecting to peripheral devices ➙ critical for embedded systems
          Inputs: Sensors
          Outputs: Actuators
Primarily, we need to know:
              How do we set up (configure) peripheral devices?
              How do we check the status of the devices?
              How do we send commands to the devices?

## Slide 11: How Does the CPU Communicate with Its Peripherals?

## Slide 12: How Does the CPU Communicate with Its Peripherals?
X

## Slide 13: How Does the CPU Communicate with Its Peripherals?
CPU
Register Memory
Peripheral
X
Bus
Bus
Bus
Bus

## Slide 14: Memory Mapped I/O
Memory Mapped I/O
Peripheral registers are mapped in memory address space at specific locations
Standard load/store access

## Slide 15: Memory Mapped I/O vs. Port Mapped I/O
Memory Mapped I/O
Peripheral registers are mapped in memory address space at specific locations
Standard load/store access
Port Mapped I/O
Port Mapped I/O
Peripheral registers are mapped to locations with their own space (separate from other memory)
Special instructions for access
May have limited addressing options

## Slide 16: Memory Mapped I/O (MMIO)
16

## Slide 19: Digital Input/Output Ports Memory Mapped Registers (x = A, B, C…)
General Purpose Input/Output port MODE Registers (GPIOx_MODER)
General Purpose Input/Output port Output TYPE Register (GPIOx_OTYPER)
General Purpose Input/Output port Pull-Up/Pull-Down Register (GPIOx_PUPDR)
General Purpose Input/Output port Input Data Register (GPIOx_IDR)
General Purpose Input/Output port Output Data Register (GPIOx_ODR)

## Slide 20: Digital Input/Output Ports Memory Mapped Registers (x = A, B, C…)
GPIO MODE Registers GPIOx_MODER Pin is input or output?
GPIO Output TYPE Register GPIOx_OTYPER Push-pull or open drain?
GPIO Pull-Up/Pull-Down Register GPIOx_PUPDR Pull-up/down resistor?
GPIO Input Data Register GPIOx_IDR Incoming data?
GPIO Output Data Register GPIOx_ODR Outgoing data?

## Slide 23: Example Memory Mapped I/O Peripheral Digital Input/Output Ports

## Slide 36
Name

## Slide 37
Name
Location in Memory

## Slide 38
Name
Location in Memory
Values automatically loaded into the
register after a reset

## Slide 39
Name
Location in Memory
Values automatically loaded into the
register after a reset
Bit
assignments

## Slide 40
Name
Location in Memory
Values automatically loaded into the
register after a reset
Bit
assignments
(r)eadable
(w)riteable

## Slide 41
Name
Location in Memory
Values automatically loaded into the
register after a reset
Bit
assignments
(r)eadable
(w)riteable
What the bits in the register will communicate
to the peripheral

## Slide 42
Name
Location in Memory
Values automatically loaded into the register after a reset
OT = Output Type
(r)eadable
(w)riteable

## Slide 43
Name
Location in Memory
Values automatically loaded into the register after a reset
OT = Output Type
(r)eadable
(w)riteable

## Slide 44
Name
Location in Memory
Values automatically loaded into the register after a reset
OT = Output Type
(r)eadable
(w)riteable

## Slide 45
Name
Location in Memory
Values automatically loaded into the register after a reset
OT = Output Type
(r)eadable
(w)riteable
What the bits in the register will communicate to the peripheral

## Slide 49
Note, bits 15..0 are not affected by reset
(r)eadable only
can not be written to

## Slide 50
(r)eadable AND
(w)riteable

## Slide 51: Access to Memory Mapped Inputs and Outputs (MMIO)
All communication with a peripheral must take place across the buses
Interface to peripheral must follow all the normal bus rules
Address bits are used to load/store data in the peripheral’s memory mapped registers
  Data bus is tri-stated except when enabled
  Control signals direct traffic
  Decoder(s) in each peripheral
  maps bits in the MM I/O registers
  to HW functionality

## Slide 52: Cortex-M4 Bus Interface
Advanced
High-performance
Bus (AHB)
Advanced Peripheral Bus (APB)

## Slide 53: Example – Writing to an External 7-Segment LED Display
The LED manufacturer specifies 8-bit values that can be written to display a character
The LED manufacturer provides a table describing the necessary value which corresponds to each character to be displayed, for example:
// LED character map
#define LEDcharP 0x0C
#define LEDcharH 0x09
#define LEDcharA 0x08
The “hardware” engineer will specify the memory address where the GPIO output register is mapped (for example 0x2020 0000)
The “software” engineer will write code to display a desired character (for example, the letter “P”)
  LDR R0,=0x20200000
  MOV R1,#0x0C
  STRB R1,[R0]

## Slide 54: Writing Code to Access MMIO Registers
Hard coding the address may pose problems in moving to a new board or microcontroller if the register address changes
          LDR R0, =0x20200000
          MOV R1, #0x0C
          STRB R1, [R0]
Rather, use the EQU assembler directive
SSEG_BASE EQU 0x20200000 // Found in giant include file
LDR R0, =BASE

## Slide 55: GPIO: General Purpose I/O
Your Nucleo board (and many such boards / microcontrollers) has about 20 GPIO pins
  Each GPIO pin is individually driven / read
A GPIO pin is connected to the bus with an I/O interface
Takes care of addressing with an address decoder
Takes care of tri-state drivers
May do additional interfacing (pull-up resistors, ...)
THIS is a GPIO pin

## Slide 56: LED: Light Emitting Diode
Semiconductor that emits photons (lights up) when current flows through
Polarized device (VANODE > VCATHODE)
Illuminates when a positive current flows from the anode to the cathode
Different colors available
Based on the energy (and voltage) required for electrons to cross the band gap
Used in Embedded Systems:
For status indicators
Remote control / communication (infra-red)
Segments in a 7-segment display
Lighting
Anode
Cathode
Flat
Edge

## Slide 57: LEDs Can Be Connected to GPIO Pins Two Ways: “Active HI” or “Active LO”
D0
D0
VOUT = HI = 5V
VOUT = LO = 0V
LED
Is On
LED
Is Off
ILED > 0A
ILED = 0A

## Slide 58: LEDs Can Be Connected to GPIO Pins Two Ways: “Active HI” or “Active LO”
+5V
D0
D0
VOUT = LO = 0V
ILED > 0A
ILED = 0A
LED
Is On
LED
Is Off
+5V
VOUT = HI = 5V

## Slide 59: LEDs Can Be Connected to GPIO Pins Two Ways: “Active HI” or “Active LO”
D0
VOUT = HI = 5V
ILED > 0A
LED
Is On
D0
VOUT = LO = 0V
ILED > 0A
LED
Is On
+5V
Usually works better
Digital GPIO
Can Sink ~ 10mA
Digital GPIO
Can Source
~ 1mA

## Slide 60: LED Current Limiting Resistor
LEDs turn on when for any time ILED > 0A
If ILED is too small, the illumination may not be visible
If ILED is too big, the LED can “burn out”
Use an appropriately sized resistor to ensure the LED current (and its visibility) are appropriate.

## Slide 61: Improving LED Current Drive
Use a GPIO to drive a transistor to increase the current flowing through one or more LEDs
VSUPPLY
Q1
D0

## Slide 62: Controlling a Matrix of LEDs
A matrix configuration reduces the number of GPIO pins required to drive multiple LEDs
For example: Turn on the top left LED
ROW GPIO PIN1 = 0V (enables LED Row1) ROW GPIO PIN2 = PIN3 = PIN4 = 5VROW ROW GPIO (disables LED Rows 2, 3, and 4)
COLUMN GPIO PIN5 = 5V (enables Column1) COLUMN GPIO PIN6 = PIN7 = PIN8 = 0V COLUMN GPIO (disables Columns 2, 3, and 4)
Quickly toggle multiple LEDs to see them all on at the same time (persistence of vision)
PIN1
PIN2
PIN3
PIN4
PIN5
PIN6
PIN7
PIN8

## Slide 63: Controlling a Matrix of LEDs
A matrix configuration reduces the number of GPIO pins required to drive multiple LEDs
For example: Turn on the top left LED
ROW GPIO PIN1 = 0V (enables LED Row1) ROW GPIO PIN2 = PIN3 = PIN4 = 5VROW ROW GPIO (disables LED Rows 2, 3, and 4)
COLUMN GPIO PIN5 = 5V (enables Column1) COLUMN GPIO PIN6 = PIN7 = PIN8 = 0V COLUMN GPIO (disables Columns 2, 3, and 4)
Quickly toggle multiple LEDs to see them all on at the same time (persistence of vision)
0V=PIN1
PIN2
PIN3
PIN4
5V=PIN5
PIN6
PIN7
PIN8

## Slide 64: Advanced Technique: "Charlieplexing" GPIO = HI or LO or “Tristated” (disconnected)
GPIO outputs can be HI, LO, or Tristated (disconnected)
With 3 possible states, we can dramatically increase the number of LEDs driven with a given number of GPIO
To illuminate LED1: PIN1 = 0V PIN2 = 5V PIN3 = Tristated (disconnected)
0V=PIN1
5V=PIN2
Tri=PIN3

## Slide 65: Advanced Technique: "Charlieplexing" GPIO = HI or LO or “Tristated” (disconnected)
65
GPIO outputs can be HI, LO, or Tristated (disconnected)
With 3 possible states, we can dramatically increase the number of LEDs driven with a given number of GPIO
To illuminate LED1: PIN1 = 0V PIN2 = 5V PIN3 = Tristated (disconnected)
0V=PIN1
5V=PIN2
Tri=PIN3
0A

## Slide 66: Advanced Technique: "Charlieplexing" GPIO = HI or LO or “Tristated” (disconnected)
66
GPIO outputs can be HI, LO, or Tristated (disconnected)
With 3 possible states, we can dramatically increase the number of LEDs driven with a given number of GPIO
To illuminate LED1: PIN1 = 0V PIN2 = 5V PIN3 = Tristated (disconnected)
0V=PIN1
5V=PIN2
Tri=PIN3
0A

## Slide 67: Advanced Technique: "Charlieplexing" GPIO = HI or LO or “Tristated” (disconnected)
67
GPIO outputs can be HI, LO, or Tristated (disconnected)
With 3 possible states, we can dramatically increase the number of LEDs driven with a given number of GPIO
To illuminate LED1: PIN1 = 0V PIN2 = 5V PIN3 = Tristated (disconnected)
0V=PIN1
5V=PIN2
Tri=PIN3
0A

## Slide 68
Buttons and Switches
68
Buttons: Momentary Connection
Switches: Maintained Connection

## Slide 69: Contact Terminology: Normal, Poles and Throws
SPST-NO
SPST-NC
A switch might be normally open (NO) or normally closed/connected (NC) to specify the default state
Poles: an electrically separate connection
Each pole is a separate circuit, a separate connection
Throw: separate wiring paths (other than "open") that the switch can adopt
Single throw: Switch is open or closed
SP: One circuit
ST: Open or closed

## Slide 70: Contact Terminology: Normal, Poles and Throws
SPST-NO
SPST-NC
SPDT
A switch might be normally open (NO) or normally closed/connected (NC) to specify the default state
Poles: an electrically separate connection
Each pole is a separate circuit, a separate connection
Throw: separate wiring paths (other than "open") that the switch can adopt
Single throw: Switch is open or closed
Double throw: Switch is connected to one side or connected to the other side
SP: One circuit
ST: Open or closed
SP: One circuit
DT: A or B
A
B

## Slide 71: Contact Terminology: Normal, Poles and Throws
SPST-NO
SPST-NC
SPDT
DPST
DPDT
A switch might be normally open (NO) or normally closed/connected (NC) to specify the default state
Poles: an electrically separate connection
Each pole is a separate circuit, a separate connection
Throw: separate wiring paths (other than "open") that the switch can adopt
Single throw: Switch is open or closed
Double throw: Switch is connected to one side or connected to the other side
SP: One circuit
ST: Open or closed
SP: One circuit
DT: A or B
A
B
DP: Two circuits
ST: Open or closed
SP: Two circuits
DT: A or B AND
C or D
A
B
C
D

## Slide 72: Connecting to a Microcontroller
The switch connects to VSUPPLY or GND to drive a 1 or 0 to the GPIO
Pin goes HI when
button is pressed
Digital
Input
Digital
Input
Pin goes LO when
button is pressed

## Slide 73: Connecting to a Microcontroller
The switch connects to VSUPPLY or GND to drive a 1 or 0 to the GPIO
What happens if the switch is open?
Pin goes HI when
button is pressed
Digital
Input
Digital
Input
Pin goes LO when
button is pressed

## Slide 74: Connecting to a Microcontroller
The switch connects to VSUPPLY or GND to drive a 1 or 0 to the GPIO
What happens if the switch is open?
It “floats” to an indeterminate value
Pin goes HI when
button is pressed
Digital
Input
Digital
Input
Pin goes LO when
button is pressed

## Slide 75: Connecting to a Microcontroller
The switch connects to VSUPPLY or GND to drive a 1 or 0 to the GPIO
What happens if the switch is open?
It “floats” to an indeterminate value
Use a pull-up or pull-down resistor to drive a voltage when switch is open
Pin goes HI when
button is pressed
Digital
Input
Digital
Input
Pin goes LO when
button is pressed

## Slide 76: Connecting to a Microcontroller
The switch connects to VSUPPLY or GND to drive a 1 or 0 to the GPIO
What happens if the switch is open?
It “floats” to an indeterminate value
Use a pull-up or pull-down resistor to drive a voltage when switch is open
Large resistance so you don't waste power when not active
500A
500A
Pin goes HI when
button is pressed
Digital
Input
Digital
Input
Pin goes LO when
button is pressed

## Slide 77: Internal GPIO Pull-Up (and Pull-Down) Resistors

## Slide 79
Buttons and Switches
79
Buttons: Momentary Connection
Switches: Maintained Connection

## Slide 80: Switch Bounce
Switches and buttons go can “bounce” when changing states
Up to 10ms (or more) when the connection is unstable
Microcontroller may count the bounces as multiple events

## Slide 81: Switch Bounce
Switches and buttons go can “bounce” when changing states
Up to 10ms (or more) when the connection is unstable
Microcontroller may count the bounces as multiple events
Solutions:
Solution 1A, HW: Use a low-pass filter (capacitor) with the button
Between HI and LO
Pin goes HI when
button is pressed
Digital
Input

## Slide 82: Switch Bounce
Switches and buttons go can “bounce” when changing states
Up to 10ms (or more) when the connection is unstable
Microcontroller may count the bounces as multiple events
Solutions:
Solution 1A, HW: Use a low-pass filter (capacitor) with the button
Solution 1B, HW: Use a low-pass filter (capacitor) with a Schmitt trigger
Pin goes HI when
button is pressed
Digital
Input
Output of Schmitt Trigger
Has Hysteresis

## Slide 83: Switch Bounce
Switches and buttons go can “bounce” when changing states
Up to 10ms (or more) when the connection is unstable
Microcontroller may count the bounces as multiple events
Solutions:
Solution 1A, HW: Use a low-pass filter (capacitor) with the button
Solution 1B, HW: Use a low-pass filter (capacitor) with a Schmitt trigger
Solution 2, HW: Use an SR-Latch with the button
SR Latch
S | R | Q (i.e. output)
0 | 0 | Hold
0 | 1 | 0
1 | 0 | 1
1 | 1 | Don't do this

## Slide 84: Switch Bounce
Switches and buttons go can “bounce” when changing states
Up to 10ms (or more) when the connection is unstable
Microcontroller may count the bounces as multiple events
Solutions:
Solution 1A, HW: Use a low-pass filter (capacitor) with the button
Solution 1B, HW: Use a low-pass filter (capacitor) with a Schmitt trigger
Solution 2, HW: Use an SR-Latch with the button
Solution 3, SW: Wait 10+ ms after detecting the change and sample again (slower = more protection)

## Slide 85: Keypads (Lots of Buttons)
Buttons are formed into a matrix to reduce GPIO connections
3x4 keypad
Only 7 GPIO pins
One for each row
One for each column

## Slide 86: Activate Rows and Test Columns
Set one Column 1 to GND, others are 5V or open
GND

## Slide 87: Activate Rows and Test Columns
Set one Column 1 to GND, others are 5V or open
Read Row1, Row2, Row3, and Row4 to see if GND
      Row 1 = GND, then “1” is pressed
GND

## Slide 88: Activate Rows and Test Columns
Set one Column 1 to GND, others are 5V or open
Read Row1, Row2, Row3, and Row4 to see if GND
      Row 1 = GND, then “1” is pressed
      Row 2 = GND, then “4” is pressed
      Row 3 = GND, then “7” is pressed
      Row 4 = GND, then “*” is pressed

## Slide 89: Activate Rows and Test Columns
Set one Column 1 to GND, others are 5V or open
Read Row1, Row2, Row3, and Row4 to see if GND
      Row 1 = GND, then “1” is pressed
      Row 2 = GND, then “4” is pressed
      Row 3 = GND, then “7” is pressed
      Row 4 = GND, then “*” is pressed
      Update a new Column to GND and repeat

## Slide 90: Liquid Crystal Display (LCD)

## Slide 91: Using the Hitachi HD44780 LCD Driver
Extremely common
Alphanumeric displays
1,2,4,8 rows by 16, 32, 40, 80 columns (1 character per position)
Handles font data: ASCII, Japanese Kana, some symbols
Backlight system
Selectable 4 or 8-bit data bus
Very, very, very low power without a backlight

## Slide 92: Using the Hitachi HD44780 LCD Driver
RS (Register Select)
  RS = LO to send Commands
  RS = HI to send Data
R/W (Read or Write)
  Pull to GND to Write data
E (Clock Enable on falling edge)
Data bus is 4-bit or 8-bits
Other pins for contrast and backlighting

## Slide 93: Initializing the Hitachi HD44780 LCD Driver
After power-on, several commands get written to initialize the device
Several timed waits are required to allow the controller to do its power-on work

## Slide 94: An Interface to the HD44780 LCD Driver
Using the HD44780 uses 7 / 11 pins
Can use a “boosterpack” between your microcontroller and the HD44780
  TI's PCF8574 (I2C)
  Microchip's MCP23017 (I2C)
  Microchip's MCP23S17 (SPI)
“Free” with a serial communication port
Non-insignificant amount of software
I2C
Serial Port

## Slide 95: Overview of Lecture
What Are Peripherals?
Memory Mapped I/O
volatile
General Purpose Inputs/Outputs
  Light Emitting Diodes (LEDs)
  Switches
  Keypads
  Liquid Crystal Displays (LCDs)