## Slide 1: 04633-A Embedded systems development Lecture 1: Overview
Emmanuel Ndashimye

## Slide 2
Emmanuel Ndashimye
PhD & HEA, AUT, 2018 (NZ) Masters, HUST,2009 (China) B.Tech, UR CST,2005 (Rwanda)
Research: Telecom (Vehicular Network), Security Systems and IoT. Research link: https://scholar.google.com/citations?user=6y_k3EgAAAAJ&hl=en

## Slide 3: Course objectives
At the end of this class, student should be able to:
  Interface a microcontroller to a variety of analog and digital input and output devices.
  Write (C and assembly language) code for a microcontroller
  Program a microcontroller to implement a closed loop automatic control.
  Wireless communication in embedded systems
  Analyze a real-world problem and develop an ES –based project for addressing the problem.

## Slide 4: Required Acquisitions
Text book
PIC microcontroller
MPLAB IDE & MPLAB Compiler & Simulator
Arduino
Sensors
Actuators (Motors)
STM32

## Slide 5: Required Acquisitions
Text book
PIC microcontroller
MPLAB IDE & MPLSB Compiler & Simulator
Arduino
Sensors
Actuators (Motors)
ESP32/ESP8266

## Slide 6: Required Acquisitions
Text book
PIC microcontroller
MPLAB IDE & MPLSB Compiler & Simulator
STM32
Sensors
Actuators (Motors)

## Slide 7: Required Acquisitions
Text book
PIC microcontroller
MPLAB IDE & MPLSB Compiler & Simulator
Arduino & Arduino IDE
Sensors
Actuators (Motors)
STM32

## Slide 8: Required Acquisitions
Text book
PIC microcontroller
MPLAB IDE & MPLSB Compiler & Simulator
Arduino
Sensors
Actuators (Motors)
ESP32/ESP8266

## Slide 9: Grading
Homework (6 LABs): 50%
Midterm exam (1): 15%
Final Project: 30%
Class participation, quizzes, reading critiques: 5%

## Slide 10: Embedded systems Overview

## Slide 11
The basic idea of an embedded system is a simple one. If we take any engineering product that needs control, and if a computer is incorporated within that product to undertake the control, then we have an embedded system.
A system whose principal function is not computational, but which is controlled by a computer embedded within it
What is an Embedded System?

## Slide 12: What is an Embedded System?
The integration of:
  Sensors
  Actuators
  Intelligence
  With a system to produce:
    More capable, versatile, and robust performance

## Slide 13: Intro to ES
An embedded system is a system whose principal function is not computational, but which is controlled by a computer embedded within it.
An embedded system is some combination of HW and SW, either fixed in capability or programmable, that is specifically designed for a particular function.
A general computer is defined not to be an embedded system
Limited Recourses: ES often must cost just a few dollars, must be sized to fit on single chip, must perform fast enough to process data in real-time, and must consume minimum power to extend battery life.

## Slide 14
The Embedded System - What Disciplines does it Involve?
Embedded Systems
Electronics
Electric Motors &
Computer Architecture
Software Engineering
Integrated Circuit
Design
Digital
Analogue
Electronics
Actuators
Sensors and
Measurements
Control
Engineering
Data
Communications

## Slide 15
Embedded Systems Concept Map

## Slide 16: Connect via peripherals
Embedded systems talk with outside word via peripherals:
  Serial communication interfaces(SCI): RS-232,RS-422, RS-485,…
  USB
  Multi Media Cards: SD Cards, Compact Flash,..
  Networks
  ADC/DAC
  Communication protocols (I2C, Serial UART, SPI)

## Slide 17: Embedded Vs PC
Embedded
Defined process and function
Application specific
Numerous ES make up the computer
Tightly constrained(Cost, Size , Performance, and Power)
PC
Generic
Manufactured with general requirement
Enough space for numerous chips and other components
No power challenge

## Slide 18: Difference between Embedded and PC app-Coding
Embedded
Closer to the Hardware
  Use native data types
  Fewer system resources
  No OS
  More efficient algorithms
    Higher frequency=higher power
PC Application
Abstracted HW
Plenty of Resources
Has OS

## Slide 19: Example of embedded Systems
Embedded Software is in every electronic device used in real life including cell phone, digital camera, calculators, oven, washing machine, fridge, etc.

## Slide 20: Administrivia
Course Website
  Check it often
  All lectures and lab handouts will be posted on Canvas
  You can see your grades here
Piazza for all discussions and announcements:
  We love questions, but DO NOT post code in public questions!
TAs
  Students with both course and hands-on experience in embedded systems
  Office hours: Faculty and TA
Lectures (80min)
  Tuesday / Thursday, 12:30 – 1:50PM, HH B103
  Textbooks – None required, a few suggestions in Syllabus

## Slide 21: Policies on Collaboration
What is okay?
  On team labs, definitely work together
Sharing your findings with others, especially over a tricky detail like a register setting…
Clarifying questions posted by other students on Piazza (no solutions or code)

## Slide 22: Cheating and Plagiarism
Your code may be compared against others!
CMU cheating policies
  Please read and understand: http://www.cmu.edu/policies/documents/Cheating.html
Cheating penalty
  Immediate “R” grade and department notification
Copyright warning
  Please do not post or otherwise redistribute material from the class
  No video or audio recording

## Slide 23: Nucleo-64 Micro-Controller Board
Nucleo-64 MCU Board
  ARM Cortex M4 Core
  84 MHz
  512KB Flash + 96KB SRAM
  Arduino Uno v3 and STM32 Connectivity
23

## Slide 24: What is an embedded system?

## Slide 25: What is an embedded system?

## Slide 26: An introduction
Computer system hidden (embedded) in other systems
  Often interacts with the physical environment
Purpose built
End users see “smart” device rather then computer
  Often the main purpose of using it is not information processing
Special-purpose vs. general-purpose computing

## Slide 27: What Is an Embedded System?
“It is any device that includes a programmable computer but is not itself intended to be a general purpose computer.”
– Wayne Wolf

## Slide 28
“It is any device that includes a programmable computer but is not itself intended to be a general purpose computer.”

## Slide 29
“It is any device that includes a programmable computer but is not itself intended to be a general purpose computer.”

## Slide 30
“It is any device that includes a programmable computer but is not itself intended to be a general purpose computer.”

## Slide 31
“It is any device that includes a programmable computer but is not itself intended to be a general purpose computer.”

## Slide 32: Car Engine Control Unit (ECU)
Functions
  Fuel injection
  Air intake setting
  Spark timing
  Exhaust gas circulation
  Electronic throttle control
Constraints
  Reliability in harsh environment
  Cost
  Weight
Many Inputs and Outputs
  Discrete sensors & actuators
  Network interface to rest of car

## Slide 33: Embedded, Everywhere

## Slide 34: Embedded, Everywhere – Internet of Things
People Connecting
Through Machines
Machines Connecting to Machines
and the Physical Environment

## Slide 35: Embedded in Your Daily Life
How many microcontrollers are around you?
  Bathroom scale with digital read out
  Iron that turns itself off automatically
  Electronic toothbrush (with ~3000 lines of code)
  Cooking range
  Laundry machine and dryer
  Toaster
  Microwave
  Home-security
  TV, cable-box, AV system
  Game console
  Thermostat
  Cars, Toys, Medical Devices…
Embedded Systems
Notes: Furby has a more powerful CPU then original mars lander

## Slide 36: Embedded in Your Daily Life
How many microcontrollers are around you?
  Bathroom scale with digital read out
  Iron that turns itself off automatically
  Electronic toothbrush (with ~3000 lines of code)
  Cooking range
  Laundry machine and dryer
  Toaster
  Microwave
  Home-security
  TV, cable-box, AV system
  Game console
  Thermostat
  Cars, Toys, Medical Devices…
Embedded Systems

## Slide 37: What is driving the embedded explosion?

## Slide 38: Moore’s Law (a statement about economics): IC transistor count doubles every 18-24 month
Photo Credit: Intel

## Slide 39: Flash memory scaling: Rise of density & volumes; Fall (and rise) of prices

## Slide 42: Not so fast! Bell’s Law of Computer Classes: A new computing class roughly every decade
year
log (people per computer)
Streaming information
to/from physical world
Number Crunching
Data Storage
productivity
interactive
Mainframe
Minicomputer
Workstation
PC
Laptop
CPSD
“Roughly every decade a new, lower priced computer class forms based on a new programming platform, network, and interface resulting in new usage and the establishment of a new industry.”
Credit: D. Culler
Notes: So if we look at the computing spectrum today, each of the classes exist simultaneously. In a room we can put 100s of teraflops and many petabytes of computing.
Our productivity, document preparation, and personal information management fits in our pocket and a new class is emerging that will provide a means of streaming information to and from the physical world like we have never seen before.

## Slide 43: Technology Trends
Multi-core embedded with System-on-a-Chip (SoC)
Better, cheaper, lower power sensors
Better communication
  Bluetooth Low-Energy
  802.15.4
  802.11 AC
  LP-WAN
Energy Harvesting / Ultra Low Power

## Slide 44: Why is embedded different?

## Slide 45: Typical Embedded System Challenges (1-2)
Small Size, Low Weight
  Hand­held electronics
  Transportation applications ­­ weight costs money
Low Power
  Battery power for 8+ hours (laptops often last only 2 hours)
  Limited cooling may limit power even if AC power available

## Slide 46: Typical Embedded System Challenges (2-2)
Harsh environment
  Heat, vibration, shock
  Power fluctuations, RF interference, lightning
  Water, corrosion, physical abuse
Safety-critical operation
  Must function correctly
  Must not function incorrectly
Extreme cost sensitivity
  $.05 adds up over 1,000,000 units

## Slide 47: CPU: An All­ Too ­Common View of Computing
Measured by: Performance
CPU

## Slide 48: An Enlightened Computer Engineer's View
Measured by: Performance, Cost
    Compilers & OS matter
CPU
Cache
Memory
I/O

## Slide 49: An Embedded Computer Designer's View
Microcontroller
Measured by: Cost, I/O connections, Memory Size, Performance
CPU
Cache
Memory
I/O
MMI
D/A
A/D

## Slide 50: Modern Embedded Systems View
Measured by: Does it actually work? (and all of the other stuff)
CPU
Cache
Memory
I/O
MMI
D/A
A/D
Microcontroller
Sensors
Actuator
Auxiliary Systems
(power, cooling)
Diagnostic
tools
External
Environment
Electro-mechanical
backup and safety
CPU
Cache
Memory
I/O
MMI
D/A
A/D
Microcontroller
Sensors
Actuator
Auxiliary Systems
(power, cooling)
Diagnostic
tools
External
Environment
Electro-mechanical
backup and safety
CPU
Cache
Memory
I/O
MMI
D/A
A/D
Microcontroller
Sensors
Actuator
Auxiliary Systems
(power, cooling)
Diagnostic
tools
External
Environment
Electro-mechanical
backup and safety
Network
Network
Network
Distributed!

## Slide 51: Embedded Systems Careers

## Slide 52
Digital Camera : An example of embedded system

## Slide 53
Example 1: The Domestic Fridge
The
Embedded
Computer
An Embedded
System
Compressor Control
Actual Temperature
Human
Interaction
20
Alarm
Display
Required Temperature
Networked
Interaction
(Maybe!)

## Slide 54
Example 2: Car Door Control, within a Larger Network

## Slide 55: Architecture of embedded systems

## Slide 56
An embedded system is a system whose principal function is not computational, but which is controlled by a computer embedded within it.
The Embedded System – Generic Block Diagram

## Slide 57
Some Computer Essentials
A computer can be simplified down to the essential elements shown.
Central
Processing
Unit (CPU)
Data
Memory
Input/
Output
Program
Memory
The
Outside
World

## Slide 58
Von Neuman and Havard Architecture

## Slide 59
A computer “executes” instructions in its Arithmetic Logic Unit (ALU), running through a series of instructions called a program. An ALU can only do a few things, but it can do them very fast. A typical 8-bit ALU can do the list shown below. A is the “Accumulator”, a digital register where the computations actually occur, and M is a location in memory. The ALU in turn forms part of the Central Processing Unit (CPU).
What can the Computer Actually Do? - Instructions and Instruction Sets

## Slide 60
Any CPU has a set of instructions that it recognizes and responds to; all programs are built up in one way or another from this instruction set. We want computers to execute code as fast as possible, but how to achieve this aim is not always an obvious matter.
One approach is to build sophisticated CPUs with exotic instruction sets, with an instruction ready for every foreseeable operation. This leads to the CISC, the Complex Instruction Set Computer. A CISC has many instructions, and considerable sophistication. Yet the complexity of the design needed to achieve this tends to lead to slow operation. One characteristic of the CISC approach is that instructions have different levels of complexity. Simple ones can be expressed in a short instruction code, say one byte of data, and execute quickly. Complex ones may need several bytes of code to define them and take a long time to execute.
A CISC machine is generally recognised by:
Many instructions (say over one hundred), some with considerable sophistication;
Instruction words are of different length;
Instructions take different lengths of time to execute.
  How Instruction Sets are Made: the “CISC” Machine

## Slide 61
Another approach is to keep the CPU very simple, and have a limited instruction set. This leads to the RISC approach – the Reduced Instruction Set Computer. The instruction set, and hence overall design, is kept simple. This leads to fast operation. One characteristic of the RISC approach is that each instruction is contained within a single binary word. That word must hold all information necessary, including the instruction code itself, as well as any address or data information also needed. A further characteristic, an outcome of the simplicity of the approach, is that every instruction normally takes the same amount of time to execute.
  How Instruction Sets are Made: the “RISC” Machine
A RISC machine is generally recognised by:
Few instructions (say well below one hundred),
Each performs a very simple action;
All instructions are single word;
All, or almost all instructions take the same length of time to execute.

## Slide 62
A microcontroller is an integrated chip that is often part of an embedded system.
Microcontroller includes a CPU, RAM, ROM, I/O ports, and timers like a standard computer
They are much smaller and simplified so that they can include all the functions required on a single chip.
The Microcontroller
Source: http://students.iitk.ac.in/eclub/assets/lectures/embedded/Embedded-Old-1.pdf

## Slide 63
A microcontroller is a microprocessor designed primarily to perform simple control functions.
Microcontrollers usually have these features
low cost,
physically small,
input/output intensive, and capable of easy interfacing,
limited memory capability for program and data,
instruction set leading to compact code, with limited arithmetic capability,
ability to operate in a real-time environment.
In certain applications the following further features are essential:
ability to operate in hostile environment, e.g. high or low temperature, tolerant to electromagnetic interference,
low power, with features adapted to battery power.
The Microcontroller

## Slide 64
Features of a General-Purpose Controller
A microcontroller = microprocessor core + memory + peripherals

## Slide 65
A Gathering of Microprocessors and Microcontrollers
PIC 16F84A
PIC 16F877
PIC 12F508
Motorola
68HC05B16
PIC 16C72
Motorola 68000

## Slide 66
PIC Microcontroller
The “PIC” was originally a design of the company General Instruments. It was intended for simple control applications, hence the name – Peripheral Interface Controller. In the late 1970s General Instruments produced the PIC1650 and PIC 1655 processors. Although the design was comparatively crude and unorthodox, the PIC was completely stand-alone, and contained some important and forward-looking features. The simple CPU was a RISC structure, with a single accumulator (called the “Working Register”, and just 30 instructions. The output pins could source or sink much more current than most other microprocessors of the time. Already the trademarks of the PIC were emerging – simplicity, stand-alone, high speed, and low cost.
General Instruments sold off its semiconductor division to a group of venture capitalists, who must have realised the immense potential of these odd little devices. Throughout the nineties the range of available PIC microcontrollers grew, and as they did so they gradually overtook many of their better-established competitors. In many cases PIC microcontrollers could run faster, needed a simpler chip-set, and were quicker to prototype with, than their competitors. Unlike many competitors, Microchip made their development tools simple, and low-cost or free. Moreover, Microchip stayed firmly entrenched in the 8-bit world.
Despite the huge advances that have been made, we can still see features of the old General Instruments PIC, even in the most recent designs.

## Slide 67
Family | Example Devices | Instruction word size | Stack size (words) | Number of instructions | Interrupt vectors
Baseline | 10F200, 12F508, 16F57 | 12-bit | 2 | 33 | None
Mid-range | 12F609, 16F84A, 16F631, 16F873A | 14-bit | 8 | 35 | 1
High Performance | 18F242, 18F2420 | 16-bit | 32 | 75, including hardware multiply | 2 (prioritised)
The PIC Microchip Families

## Slide 68
PIC 12F508/509

## Slide 69
An embedded system is a product that has one or more computers embedded within it, which exercise primarily a control function.
The embedded computer is usually a microcontroller: a microprocessor adapted for embedded control applications.
Microcontrollers are designed according to accepted electronic and computer principles, and are fundamentally made up of microprocessor core, memory and peripherals; it is important to be able to recognize their principal features.
Microchip offers a wide range of microcontrollers, divided into several different families. Each family has identical (or very similar) central architecture and instruction set. However, common features also appear across all their microcontrollers, and knowledge of one family can lead with ease to knowledge of another.
End of Lecture One
Take home slide