## Slide 1: Introduction to PIC I/O Ports + Hardware and circuits
Lecture3

## Slide 2
Almost any embedded system needs to transfer digital data between its CPU and the outside world. This transfer falls into a few categories, which can be summarised as:
Direct user interface, including switches, keypads, light emitting diodes (LEDs) and displays;
Input measurement information, from external sensors, possibly being acquired through an analogue to digital converter;
Output control information, for example to motors or other actuators;
Bulk data transfer to or from other systems or sub-systems, moving in serial or parallel form, for example sending serial data to an external memory.
How can we provide the required interface between the microcontroller core and the outside world? More precisely, how do we get the data onto or off the data bus at the right moment?
Why Digital Input/Output?

## Slide 3
Parallel Input/Output 2
We could apply a circuit like this for output.
Here a pulse on the Port Select line captures data on the bus at that instant and transfers it to the external pin.
Data Bus
External Pin
Port Select
Q
D
Two lines of
External Pin
Q
D
Read/Write
Flip-flop latches data bus value onto
external pin, when memory location
is selected, AND Write is active
high whenever
port address is
selected

## Slide 4
Parallel Input/Output 2
Data Bus
External Pin
Port Select
Two lines of
buffer transfers logic value on external pin
onto data bus line, when memory location
is selected, AND Read is active
External Pin
Read/Write
Or we could apply a circuit like this for input.
Here a pulse on the Port Select line transfers data on the external pin at that instant to the data bus.

## Slide 5
A Bi-Directional Port Pin Driver Circuit
We could combine both circuits into one multi-function circuit, like this. You don’t need to grasp all the detail of this circuit, although it’s neat if you can.
There is now an extra flip-flop, labelled “Direction”. The state of this decides in which direction data will flow.
The two flip-flops shown can each form one bit in an SFR, which can be controlled from the CPU.
A group of these bits, each driven by a circuit like this, is called a “port”
D
Q
D
Q
"Direction"
"Data"
I/O Pin
Read/Write
Port Select
Direction Select
Data Bus
(bit n of an
8
-
bit port)
(bit n)
Output Buffer
Input Buffer
Alternate Input
Function
"Data" SFR
"Direction" SFR
Read Port
Write
Port
Write
DDR
buffer, enabled
when pin is output
determines whether port
bit is input or output
8 of these flip
-
flops form
the "Data Direction" SFR
8 of these
the "Data" SFR
holds bit
output value
flip
-
flops form
D
Q
D
Q
"Direction"
"Data"
I/O Pin
Read/Write
Port Select
Direction Select
Data Bus
(bit n of an
8
-
bit port)
(bit n)
Output Buffer
Input Buffer
Alternate Input
Function
"Data" SFR
"Direction" SFR
Read Port
Write
Port
Write
DDR
buffer, enabled
when pin is output
determines whether port
bit is input or output
8 of these flip
-
flops form
the "Data Direction" SFR
8 of these
the "Data" SFR
holds bit
output value
-
flip-flops form

## Slide 6: Electrical Circuits basics

## Slide 7: Reimagined Ohm’s Law: V = IR
Positive current flows from a high potential to a low potential
Vpos to neg = Iinto pos R
Iinto pos = Vpos to neg / R
Iinto pos = (5V – 0V) / 1kΩ = 5mA
+
V
–
5mA = I
0V
5V

## Slide 8: Voltage Sources Only Have One Job
All practical power supplies are NOT ideal voltage sources
0V
5V
Rbattery
35Ω
+
V
–
I

## Slide 9: Voltage Sources Only Have One Job
All practical power supplies are NOT ideal voltage sources
Iinto pos = Vpos to neg / R
Iinto pos = (5V – 0V) / (1kΩ + 35Ω )
Iinto pos = 4.83mA
0V
5V
Rbattery
35Ω
+
V
–
4.83mA = I

## Slide 10: Voltage Sources Only Have One Job
All practical power supplies are NOT ideal voltage sources
Iinto pos = Vpos to neg / R
Iinto pos = (5V – 0V) / (1kΩ + 35Ω )
Iinto pos = 4.83mA
VOUT = (4.83mA)(1kΩ)
VOUT = 4.83V
0V
5V
Rbattery
35Ω
+
V
–
4.83mA = I
4.83V

## Slide 11: Voltage Sources Only Have One Job
All practical power supplies are NOT ideal voltage sources
Iinto pos = Vpos to neg / R
Iinto pos = (5V – 0V) / (1kΩ + 35Ω )
Iinto pos = 4.83mA
VOUT = (4.83mA)(1kΩ)
VOUT = 4.83V
Voltage Divider
0V
5V
Rbattery
35Ω
+
V
–
4.83mA = I
4.83V

## Slide 12: Kirchhoff’s Voltage Law:
What goes up, has to come down
VSUPPLY = V1 + V2
VSUPPLY
R1
R2
+
V1
–
+
V2
–

## Slide 13: Kirchhoff’s Voltage Law:
What goes up, has to come down
VSUPPLY = V1 + V2
Current goes into positive terminals
V1 = IR1
V2 = IR2
VSUPPLY
R1
R2
+
V1
–
+
V2
–
I

## Slide 14: Kirchhoff’s Voltage Law:
What goes up, has to come down
VSUPPLY = V1 + V2 = IR1 + IR2
Current goes into positive terminals
V1 = IR1
V2 = IR2
VSUPPLY
R1
R2
+
V1
–
+
V2
–
I

## Slide 15: Kirchhoff’s Voltage Law:
What goes up, has to come down
VSUPPLY = V1 + V2 = IR1 + IR2
Current goes into positive terminals
V1 = IR1 = VSUPPLY – VOUT
V2 = IR2 = VOUT – 0V = VOUT
VSUPPLY
R1
R2
+
V1
–
+
V2
–
I
VOUT
VSUPPLY
0V

## Slide 16: Kirchhoff’s Voltage Law:
What goes up, has to come down
VSUPPLY = V1 + V2 = IR1 + IR2
Current goes into positive terminals
V1 = IR1 = VSUPPLY – VOUT
V2 = IR2 = VOUT – 0V = VOUT
Sources, too: VSUPPLY = VSUPPLY – 0V
VSUPPLY
R1
R2
+
V1
–
+
V2
–
I
VOUT
VSUPPLY
–I
0V

## Slide 17: Kirchhoff’s Current Law:
What goes in, has to come out
I1 = I2 + I3
R1
R2
R3
I2
I3
I1

## Slide 18: Ohm’s Law, KVL, and KCL:
KVL
VSUPPLY = V1 + VOUT
VSUPPLY
R1
R2
+
V1
–
+
VOUT
–
VOUT
R3
I1
I2
I3

## Slide 19: Ohm’s Law, KVL, and KCL:
KVL and KCL
VSUPPLY = V1 + VOUT
I1 = I2 + I3
VSUPPLY
R1
R2
+
V1
–
+
VOUT
–
VOUT
R3
I1
I2
I3

## Slide 20: Ohm’s Law, KVL, and KCL:
KVL and KCL and Ohm’s Law
VSUPPLY = V1 + VOUT
I1 = I2 + I3
V1 = I1R1
VOUT = I2R2 = I3R3
VSUPPLY
R1
R2
+
V1
–
+
VOUT
–
VOUT
R3
I1
I2
I3

## Slide 21: Buttons and Switches: Normally Open or Normally Closed
Normally Open Button
(Push to Close)
Normally Closed Button
(Push to Open)
Normally Open Switch
(Push to Close)
Normally Closed Switch
(Push to Open)

## Slide 22: Engineering: “Doing Something Better”
Normally Open
Single Throw
(ST)
Singe
Pole (SP)
Poles: an electrically separate connection
Each pole is a separate circuit
Throw: separate wiring paths (other than "open") that the switch can connect two
  ST: Switch is open or closed
  DT: Switch is connected to “OUT1” or “OUT2”
Normally Closed
Single Throw
(ST)
Singe
Pole (SP)
Singe
Pole (SP)
DualThrow
(DT)
SPST-NO
SPST-NC
SPDT

## Slide 23: Buttons and Switches: Need Pull-Up or Pull-Down Resistors
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN

## Slide 24: Buttons and Switches: Need Pull-Up or Pull-Down Resistors Switches Open
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN
0A
0A

## Slide 25: Buttons and Switches: Need Pull-Up or Pull-Down Resistors Switches Open
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN
0A
0A
0A
0A

## Slide 26: Buttons and Switches: Need Pull-Up or Pull-Down Resistors Switches Open
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN
0A
0A
0A
0A
0A
0A

## Slide 27: Buttons and Switches: Need Pull-Up or Pull-Down Resistors Switches Open
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN
0A
0A
0A
0A
0A
0A
+
0V
–
+
0V
–

## Slide 28: Buttons and Switches: Need Pull-Up or Pull-Down Resistors Switches Open
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN
0A
0A
0A
0A
0A
0A
+
0V
–
+
0V
–
0V
VDD

## Slide 29: Buttons and Switches: Need Pull-Up or Pull-Down Resistors Switches Open or Switches Closed
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN
+
0V
–
+
0V
–

## Slide 30: Buttons and Switches: Need Pull-Up or Pull-Down Resistors Switches Open or Switches Closed
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN
+
0V
–
+
0V
–
VDD
0V

## Slide 31: Buttons and Switches: Need Pull-Up or Pull-Down Resistors Switches Open or Switches Closed
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN
+
0V
–
+
0V
–
VDD
0V
0A
0A

## Slide 32: Buttons and Switches: Need Pull-Up or Pull-Down Resistors Switches Open or Switches Closed
MCU
Pin
MCU
Pin
IN
IN
VDD
VDD
IN
IN
IN
IN
+
0V
–
+
0V
–
VDD
0V
I
I
0A
0A
I = VDD / R
Ploss = I 2R
I = VDD / R
Ploss = I 2R

## Slide 33
a) Gate Output Sourcing b) Gate Output Sinking
Current to LED Current from LED
Driving LEDs from Logic Gates (and hence Port Bit Outputs)
Data for the 16F84A (when powered from 5V) shows an output resistances of approximately 130 when at logic high, and 36 when at logic 0.
I
R
D
I
R
V
D
D
V
S
V
D
current flows out of the gate
and lights led when output
is at logic 1
current flows into gate
and lights led when
output is at logic 0

## Slide 34
Simple Digital Interfacing – connecting to switches
Connecting switches to logic inputs. (a) SPDT connection. (b) SPST with pull-up resistor.
(c) SPST with pull-down resistor
Notes: SPDT: Single Pole Double Throw (SPDT)

## Slide 35: Keypads: Detect Any Button Pressed
….
MCU
Pin
IN
VDD

## Slide 36: Keypads: Detect Each Button Pressed
“0”

## Slide 37: Keypad Decoder Circuit

## Slide 38: Keypad Decoder Circuit
COL1
COL2
COL3
COL4
ROW1
ROW2
ROW3
ROW4
Use internal
pull-up
resistors

## Slide 39: Keypad Decoder Circuit
COL1
COL2
COL3
COL4
ROW1
ROW2
ROW3
ROW4
Use internal
pull-up
resistors

## Slide 40: Making Input Signals Bigger with Operational Amplifiers (Op Amps)
Ideal Operational Amplifier MODEL 1) V+ = V- 2) I+ = I- = 0A 3) VOUT makes 1 and 2 true

## Slide 41
VOUT
2mV
1kΩ
1MΩ
Making Small Analog Signals Bigger
Notes: Here’s an operational amplifier circuit. We are asked to analyze the circuit to find the voltage, the V out, at the output pin.
Again, using our three laws of ideal Op amps, Ohm’s law, KCl, and KVL, this is pretty straightforward. But again, it does have a number of small steps.

## Slide 42
VOUT
0mV
0mV
2mV
1kΩ
1MΩ
Making Small Analog Signals Bigger
Notes: To begin with, I always look for any ground connections in the circuit.
If no node has been designated as ground, feel free to pick one.
Here, we have two grounds indicated in our circuit. Go ahead and label all of the grounds potential at 0 V.

## Slide 43
VOUT
0mV
2mV
1kΩ
1MΩ
0mV
Making Small Analog Signals Bigger
Notes: Next, I usually look to see if there are any voltage sources. Remember, voltage sources just have one job.
And this two millivolt source?

## Slide 44
VOUT
0mV
2mV
2mV
1kΩ
1MΩ
0mV
Making Small Analog Signals Bigger
Notes: It just boosts the potential as positive terminal to a positive 2 mV. That’s it’s one job

## Slide 45
1) V+ = V-
2mV
2mV
VOUT
0mV
2mV
1kΩ
1MΩ
0mV
Making Small Analog Signals Bigger
Notes: Awesome. Let’s remember, the first rule of ideal op amps. The V positive and the negative terminals will be at the same potential.
Therefore, the V negative terminal must also be at a potential of positive 2 mV. That’s just how operational amplifier circuits work

## Slide 46
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
0A
0mV
2mV
1kΩ
1MΩ
0mV
Making Small Analog Signals Bigger
Notes: Next,, we also know that 0A of current flows into or out of either one of the two op amp inputs. Therefore, we write I positive is equal to I negative is equal to 0A.
At times, this is drawn as a bidirectional arrow like this.

## Slide 47
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
2mV
1kΩ
1MΩ
0mV
Making Small Analog Signals Bigger
Notes: Now let’s look at the third rule of ideal operatives. The voltage at the op amp output will adjust itself to make the V- input pin 2 mV, the same as V positive.
Okay, but how does it do that?
We may not know yet, but we can figure it out with some combination of Ohm’s law, KCl and KVL.

## Slide 48
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
IA
2mV
1kΩ
1MΩ
IB
0mV
Making Small Analog Signals Bigger
Notes: Let’s go ahead and label currents flowing through the 1 kohm and 1Mohm resistor. We don’t values are yet, but we expect that we will have some current. Therefore, we just give them temporary names of I sub A and I sub B.

## Slide 49
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
IA
By Ohm’s Law:
IA = (2mV – 0V)/1kΩ = 2A
2mV
1kΩ
1MΩ
IB
0mV
Making Small Analog Signals Bigger
Notes: We actually have all the information we need to calculate the current I A. We can simply use Ohm’s law.
The current IA flows down from a potential of 2 mV to ground, or 0 V. That’s a positive 2 mV drop across a 1 kohm resistor.
By Ohm’s law, 2mV divided by 1kohm gives us a current IA equal to positive 2 µA.
2 µA may seem fairly small, and some students worry if their answers look like this. However, that’s one of the huge advantages of operational amplifiers. They can work on very very low current levels, and therefore, they can be quite energy efficient.

## Slide 50
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
IA = 2A
By Ohm’s Law:
IA = (2mV – 0V)/1kΩ = 2A
2mV
1kΩ
1MΩ
IB
0mV
Making Small Analog Signals Bigger
Notes: So let’s go ahead and put the 2 µA of current down on our schematic.

## Slide 51
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
By Ohm’s Law:
IA = (2mV – 0V)/1kΩ = 2A
2mV
1kΩ
1MΩ
IA = 2A
IB
0mV
Making Small Analog Signals Bigger
Notes: Hey, with this new information, we know two of the three currents flowing into this node.

## Slide 52
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
By Ohm’s Law:
IA = (2mV – 0V)/1kΩ = 2A
Since I- = 0A:
By KCL:
2mV
1kΩ
1MΩ
IA = 2A
IB
0mV
Making Small Analog Signals Bigger
Notes: KCl is actually pretty simple here, since one of the three currents is 0 A.

## Slide 53
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
By Ohm’s Law:
IA = (2mV – 0V)/1kΩ = 2A
Since I- = 0A:
By KCL: IA = IB = 2A
2mV
1kΩ
1MΩ
IA = 2A
2A=IB
0mV
Making Small Analog Signals Bigger
Notes: That means that the current IB must be equal to the current IA. They are both 2 µA!

## Slide 54
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
By Ohm’s Law:
IA = (2mV – 0V)/1kΩ = 2A
Since I- = 0A:
By KCL: IA = IB = 2A
2mV
1kΩ
1MΩ
IA = 2A
2A=IB
0mV
Making Small Analog Signals Bigger
– V +

## Slide 55
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
By Ohm’s Law:
IA = (2mV – 0V)/1kΩ = 2A
Since I- = 0A:
By KCL: IA = IB = 2A
By Ohm’s Law:
2mV
1kΩ
1MΩ
0mV
Making Small Analog Signals Bigger
IA = 2A
2A=IB
– V +
Notes: You bet. A total of 2 µA is flowing through the 1 megohms resistor.
That 2 µA of current is flowing from the output voltage, V out, down to a potential of positive 2 mV.
Therefore, the voltage change across the resistor must be equal to V out -2 mV.
By Ohm’s law we have V out -2 mV must be equal to 2 µA times one Mohm

## Slide 56
1) V+ = V-
2mV
2mV
2) I+ = I- = 0A
0A
VOUT
3) VOUT makes 1 and 2 true
0A
0mV
By Ohm’s Law:
IA = (2mV – 0V)/1kΩ = 2A
Since I- = 0A:
By KCL: IA = IB = 2A
By Ohm’s Law:
2mV
1kΩ
1MΩ
0mV
Making Small Analog Signals Bigger
– V +
IA = 2A
2A=IB
Notes: Solving this equation, we calculate an op amp output voltage of 2.002 Volts.
We did it!
This circuit is multiplying the very small input signal of 2 mV over 1000 to create an output voltage of 2.002 V.
Hooray!

## Slide 57
Modelling a Logic Gate Output
a) Generalised Model b) Model of CMOS Logic Gate Output
R
R
S(high)
S(low)
V
L
V
LH
V
LL
R
R
S(high)
S(low)
V
L
V
S
switch is in this
position when
output is at Logic 1
switch is in this
position when
output is at Logic 0
internal Logic 1 voltage
is the supply voltage
internal Logic 0
voltage is ground
To connect the port bit output, we need an understanding of how its internal circuit behaves electrically. We can model it as shown.

## Slide 58
SFRs for the 16F84A Parallel Ports
The Port SFRs can be seen in the memory map, the detail repeated here.
SFR named PORTX holds the input/output data for the port, ie it holds all the “Data Latch” bits for that port.
The SFR named TRISX holds all the “TRIS Latch” bits for that port. The bits can be set independently, so one can be input while another output. They cannot be both at the same time.
Ports A and B can easily be found on the pin connection diagram. Port A is only 5 bits, while Port B is 8.
Note that some pins have several functions, as indicated on the diagram.